## Slide 1: Introduction to Tracking Part 2

## Slide 2: Object Detection
Detecting objects to be tracked

## Slide 3: Can we segment particles this way?
If background is uniform and all exhibit similar intensity
Even then, not ideal:
  Adjacent particles conjoined
  Loss of localisation accuracy

## Slide 4: Local maxima detection

## Slide 5: Gaussian Filtering is the basis for blob detection
For larger objects, a Laplacian-of-Gaussian (LoG) works quite well
  Needs sufficient spatial resolution for edge detector
For smaller objects, a Difference-of-Gaussians (DoG) is better.
  Rough approximation of LoG

## Slide 6: Effect of LoG Filtering
33 | 21 | 54 | 25 | 36 | 24 | 31 | 8 | 19 | 50 | 22 | 18 | 15 | 25 | 25
17 | 34 | 13 | 26 | 31 | 43 | 31 | 23 | 37 | 26 | 34 | 25 | 20 | 44 | 32
26 | 33 | 23 | 17 | 27 | 24 | 32 | 37 | 34 | 28 | 36 | 49 | 34 | 36 | 31
23 | 18 | 44 | 22 | 49 | 38 | 42 | 34 | 25 | 41 | 29 | 39 | 30 | 36 | 28
12 | 24 | 27 | 17 | 42 | 30 | 30 | 20 | 34 | 29 | 44 | 29 | 24 | 26 | 47
37 | 30 | 38 | 1 | 29 | 26 | 41 | 84 | 22 | 29 | 30 | 41 | 33 | 6 | 31
20 | 36 | 23 | 18 | 30 | 29 | 65 | 83 | 72 | 29 | 4 | 35 | 34 | 30 | 34
47 | 30 | 29 | 16 | 23 | 46 | 75 | 84 | 81 | 44 | 28 | 31 | 15 | 23 | 41
24 | 43 | 22 | 0 | 25 | 31 | 65 | 83 | 58 | 39 | 18 | 30 | 31 | 16 | 29
27 | 47 | 40 | 37 | 29 | 34 | 46 | 40 | 48 | 30 | 11 | 40 | 27 | 29 | 13
53 | 30 | 23 | 28 | 36 | 20 | 41 | 30 | 29 | 18 | 40 | 37 | 28 | 18 | 42
24 | 51 | 23 | 31 | 28 | 26 | 18 | 29 | 34 | 43 | 50 | 23 | 28 | 29 | 36
41 | 46 | 29 | 32 | 23 | 34 | 36 | 29 | 30 | 24 | 6 | 34 | 39 | 32 | 27
25 | 24 | 22 | 14 | 21 | 33 | 27 | 41 | 26 | 27 | 29 | 49 | 38 | 32 | 37
44 | 33 | 23 | 28 | 34 | 58 | 22 | 15 | 38 | 50 | 15 | 22 | 26 | 29 | 35
34 | 35 | 38 | 39 | 38 | 37 | 33 | 33 | 34 | 33 | 34 | 37 | 33 | 28 | 25
35 | 37 | 38 | 37 | 37 | 37 | 36 | 36 | 37 | 35 | 36 | 37 | 34 | 30 | 25
38 | 37 | 36 | 36 | 35 | 33 | 31 | 31 | 33 | 33 | 34 | 37 | 37 | 34 | 30
35 | 34 | 35 | 35 | 32 | 27 | 21 | 19 | 20 | 23 | 28 | 33 | 37 | 38 | 35
33 | 34 | 35 | 34 | 27 | 17 | 10 | 7 | 8 | 11 | 19 | 28 | 33 | 35 | 35
36 | 37 | 37 | 32 | 20 | 7 | 2 | 3 | 2 | 3 | 11 | 23 | 31 | 34 | 34
37 | 38 | 37 | 28 | 13 | 2 | 3 | 13 | 8 | 0 | 6 | 19 | 30 | 35 | 36
35 | 35 | 34 | 24 | 10 | 2 | 10 | 29 | 16 | 1 | 5 | 18 | 30 | 36 | 38
37 | 36 | 32 | 22 | 11 | 4 | 10 | 17 | 8 | 0 | 6 | 20 | 31 | 37 | 39
37 | 38 | 32 | 23 | 14 | 7 | 5 | 4 | 2 | 3 | 12 | 24 | 33 | 38 | 39
35 | 37 | 35 | 27 | 19 | 12 | 8 | 6 | 7 | 12 | 20 | 30 | 36 | 38 | 37
34 | 35 | 36 | 31 | 25 | 20 | 18 | 17 | 19 | 23 | 29 | 35 | 38 | 38 | 37
34 | 34 | 36 | 35 | 31 | 29 | 27 | 27 | 28 | 30 | 34 | 37 | 38 | 37 | 36
34 | 35 | 36 | 36 | 35 | 34 | 34 | 33 | 32 | 33 | 35 | 36 | 37 | 35 | 33
36 | 35 | 36 | 37 | 36 | 36 | 37 | 36 | 34 | 34 | 35 | 36 | 37 | 33 | 30

## Slide 7: Effect of DOG Filtering
33 | 21 | 54 | 25 | 36 | 24 | 31 | 8 | 19 | 50 | 22 | 18 | 15 | 25 | 25
17 | 34 | 13 | 26 | 31 | 43 | 31 | 23 | 37 | 26 | 34 | 25 | 20 | 44 | 32
26 | 33 | 23 | 17 | 27 | 24 | 32 | 37 | 34 | 28 | 36 | 49 | 34 | 36 | 31
23 | 18 | 44 | 22 | 49 | 38 | 42 | 34 | 25 | 41 | 29 | 39 | 30 | 36 | 28
12 | 24 | 27 | 17 | 42 | 30 | 30 | 20 | 34 | 29 | 44 | 29 | 24 | 26 | 47
37 | 30 | 38 | 1 | 29 | 26 | 41 | 84 | 22 | 29 | 30 | 41 | 33 | 6 | 31
20 | 36 | 23 | 18 | 30 | 29 | 65 | 83 | 72 | 29 | 4 | 35 | 34 | 30 | 34
47 | 30 | 29 | 16 | 23 | 46 | 75 | 84 | 81 | 44 | 28 | 31 | 15 | 23 | 41
24 | 43 | 22 | 0 | 25 | 31 | 65 | 83 | 58 | 39 | 18 | 30 | 31 | 16 | 29
27 | 47 | 40 | 37 | 29 | 34 | 46 | 40 | 48 | 30 | 11 | 40 | 27 | 29 | 13
53 | 30 | 23 | 28 | 36 | 20 | 41 | 30 | 29 | 18 | 40 | 37 | 28 | 18 | 42
24 | 51 | 23 | 31 | 28 | 26 | 18 | 29 | 34 | 43 | 50 | 23 | 28 | 29 | 36
41 | 46 | 29 | 32 | 23 | 34 | 36 | 29 | 30 | 24 | 6 | 34 | 39 | 32 | 27
25 | 24 | 22 | 14 | 21 | 33 | 27 | 41 | 26 | 27 | 29 | 49 | 38 | 32 | 37
44 | 33 | 23 | 28 | 34 | 58 | 22 | 15 | 38 | 50 | 15 | 22 | 26 | 29 | 35
1 | 1 | 1 | 1 | 1 | 2 | 1 | 1 | 2 | 1 | 2 | 2 | 1 | 0 | 1
1 | 2 | 2 | 1 | 1 | 2 | 2 | 2 | 1 | 1 | 2 | 1 | 1 | 1 | 1
3 | 2 | 1 | 0 | 0 | 2 | 3 | 4 | 3 | 2 | 2 | 2 | 2 | 1 | 2
2 | 1 | 0 | 0 | 2 | 3 | 3 | 2 | 2 | 3 | 4 | 3 | 2 | 1 | 2
1 | 1 | 0 | 1 | 4 | 4 | 1 | 2 | 1 | 2 | 5 | 3 | 1 | 0 | 1
2 | 1 | 1 | 3 | 5 | 2 | 4 | 9 | 7 | 2 | 2 | 3 | 1 | 0 | 0
2 | 1 | 1 | 4 | 3 | 3 | 11 | 17 | 15 | 7 | 1 | 3 | 2 | 0 | 0
1 | 1 | 2 | 4 | 2 | 5 | 15 | 21 | 19 | 9 | 2 | 3 | 2 | 1 | 0
2 | 2 | 3 | 3 | 1 | 5 | 13 | 18 | 15 | 6 | 1 | 3 | 2 | 1 | 1
1 | 2 | 3 | 2 | 1 | 4 | 7 | 9 | 6 | 2 | 2 | 3 | 2 | 1 | 0
1 | 2 | 3 | 2 | 1 | 1 | 1 | 1 | 1 | 2 | 5 | 4 | 2 | 0 | 0
1 | 1 | 2 | 3 | 2 | 2 | 2 | 2 | 2 | 3 | 3 | 2 | 1 | 0 | 0
0 | 1 | 1 | 2 | 2 | 2 | 2 | 2 | 1 | 1 | 1 | 0 | 1 | 1 | 1
0 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 0 | 0 | 0 | 0 | 1 | 1 | 2
0 | 0 | 1 | 2 | 1 | 0 | 0 | 0 | 0 | 1 | 1 | 0 | 1 | 2 | 1

## Slide 8: Tracking Cells
A few things to bear in mind

## Slide 9
Implicitly tracks cells from frame to frame
Can deal with a certain amount of cell-cell contact
Morphology of cells can be measured at each frame
Frame rate needs to be high
High cell density will cause problems

## Slide 12: Other methods

## Slide 13: Trajectory Construction
How do we link detections to make tracks?

## Slide 14
 | X | Y
1 | 54.714 | 52.262
2 | 55.046 | 52.466
3 | 55.197 | 52.539
4 | 55.134 | 52.602
5 | 54.971 | 52.858
6 | 54.894 | 53.022
7 | 54.339 | 53.402
8 | 53.569 | 53.593
9 | 53.22 | 54.242
10 | 53.125 | 54.075
Chart: Y

## Slide 15
 | X | Y
1 | 14.5 | 12.5
2 | 15.5 | 12.5
3 | 15.5 | 12.5
4 | 13.5 | 12.5
5 | 14.5 | 13.5
6 | 13.5 | 13.5
7 | 14.5 | 13.5
8 | 13.5 | 14.5
9 | 13.5 | 14.5
10 | 14.5 | 14.5
Chart: Y

## Slide 16: What if you want to track more than one object?
Simplest is nearest neighbour approach
Works for sparse population and high frame rate
t1
t2
t1
t2

## Slide 17: Joining the dots
Situation is usually more complicated
t1
t1
t1
t1
t1
t1

## Slide 18: Joining the dots
Situation is usually more complicated
t2
t2
t2
t2
t2
t2

## Slide 19: Joining the dots
Situation is usually more complicated
t3
t3
t3
t3
t3
t3

## Slide 20: Joining the dots
Situation is usually more complicated
t1
t2
t1
t2
t1
t1
t2
t2
t1
t2
t1
t2
t3
t3
t3
t3
t3
t3

## Slide 21: Let’s formalise this a little
P1
t1
P1
t2
P2
t1
P2
t2
Need information about particles to construct trajectories:
  Minimum amount of info is coordinates:
    P1 = (x1, y1), P2 = (x2, y2)
  Think of this as the set of “features”
When constructing trajectories, evaluate differences between features:
Trajectories are constructed in a way that minimises these differences

## Slide 22: building trajectories works like so…
For each particle in frame 1:
  For each particle in frame 2:
    Compile features for each particle and calculate distance:
  Link particle in frame 2 with lowest value for d.
t1
t2
t1
t2
8
2
10
3

## Slide 23: building trajectories works like so…
For each particle in frame 1:
  For each particle in frame 2:
    Compile features for each particle and calculate distance:
  Link particle in frame 2 with lowest value for d.
t1
t2
t1
t2
8
10

## Slide 24
Multiple associations can quickly become computationally challenging
P1
t1
P1
t2
P2
t1
P2
t2
P3
t1
P3
t2
P3
t1
P3
t2
But, can eliminate the least probable links

## Slide 25: Positional Information often insufficient
t1
t2
t1
t2
t1
t1
t2
t2
t1
t2
t1
t2
t3
t3
t3
t3
t3
t3

## Slide 26
t1
t2
t1
t2
t1
t1
t2
t2
t1
t2
t1
t2
t3
t3
t3
t3
t3
t3
A Priori information can help in “busy” fields of view
For example, if motion is approximately linear and processive…

## Slide 27: This is the basis for Kalman filtering
If motion is predictable, we can include “predicted” position as a feature
t1
t2
t1
t2
t1
t2
t3
t3
t3
t3
t3
t3

## Slide 28
Complexity can be reduced through choice of imaging conditions
If frame rate is sufficiently high, such that displacement is small relative to object size, tracking becomes trivial
t1
t2
t1
t2
t1
t1
t2
t2
t1
t2
t1
t2
t3
t3
t3
t3
t3
t3
t1
t2
t3
t1
t2
t3
t1
t2
t3
t1
t2
t3

## Slide 29: Common Problems
Localisation Error
  Influences displacement/velocity measures
All the dots look the same!
  Number of available features is small
Motion is often not predictable
  Or at least, it is not known beforehand
Missed detections
  Breaks in trajectories are commonplace
  Need some approach to “bridging gaps”

## Slide 30
Despite best efforts, gaps in trajectories will exist!
t1
t1
t1

## Slide 31
Despite best efforts, gaps in trajectories will exist!
t2
t2

## Slide 32
Despite best efforts, gaps in trajectories will exist!
t3
t3

## Slide 33
Despite best efforts, gaps in trajectories will exist!
t4
t4
t4

## Slide 34
Despite best efforts, gaps in trajectories will exist!
t1
t2
t1
t2
t1
t2
t3
t3
t3
t4
t4
t4

## Slide 35
Most tracking plugins will attempt to bridge gaps.
It may be necessary to adjust either
  Detection parameters
  Linking parameters
Can introduce spurious detections/links
Errors cannot be eliminated, only minimised.
t1
t2
t3
t4
t2
t3
t4

## Slide 36: Quiz 4 – Problematic Data set
Open the file in the Quiz 4 folder
List everything that would prevent you tracking the dots accurately

## Slide 37: Demo 5 – Trackmate

## Slide 38: Challenge 1 – Using TrackMate
Open the Challenge 1 folder – there are two datasets inside.
Track both with TrackMate – which dataset has the higher mean speed?

## Slide 40: Analysing Trajectories
Once tracked, what numbers can we extract?

## Slide 41: Analysing trajectories
Velocity
  Instantaneous velocity (v1, v2, v3 … vn)
  Mean velocity
Directionality
  Different definitions
  One Example:
Run Length
  Velocity may frequently be zero
  Intermittent non-zero velocities result in start-stop-start motion
  Run length defines distance travelled between “stops”
Mean Square Displacement (MSD)
t1
t2
t3
t4
Δt1
Δx1
v1
Δt2
Δx2
v2
Δt3
Δx3
v3
ΔT
ΔX
V

## Slide 42: Sources of error
Total displacement
  Influenced by localisation error
  Stationary particles have non-zero displacement
Velocity
  How to deal with “stop-go” motion?
  Velocity is rarely zero
Run Length
  How to define? What constitutes positive velocity?
Mean Square Displacement
  Strongly influenced by noise

## Slide 43: Challenge 2 – Interpreting results
Open the Challenge 2 folder – there are three datasets.
Track all with TrackMate - what is mean speed of the particles in each dataset?
Is mean speed the best metric to show differences between the datasets? Can you think of a better metric?

## Slide 45: Mean Square Displacement
Characterises nature of motility
  Active
  Pure Diffusion
  Confined
t1
t2
t3
t4
t5
Δx1
Δx2
Δx3
Δx4
Δx1
Δx2
Δx1
Chart: Time Step
| 0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12
Confined | 0 | 0.69315 | 1.0986 | 1.3863 | 1.6094 | 1.7918 | 1.9459 | 2.0794 | 2.1972 | 2.3026 | 2.3979 | 2.4849 | 2.5649
Diffuse | 0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12
Active Motility | 0 | 1 | 2.4623 | 4.1712 | 6.0629 | 8.1033 | 10.2706 | 12.5495 | 14.9285 | 17.3986 | 19.9526 | 22.5845 | 25.2892